## Slide 1
A Modular Python Framework for Mechanically Pumped Loop Simulation
MPL modelling requires physically transparent coupling of pressure, enthalpy, mass flow, phase change, accumulator pressure reference, and empirical closures.
Context and motivation
• MPL2030 programme: thermal control of spacecraft and high-power electronics
• Two-phase loops couple compressible accumulator dynamics, pump hydraulics,
phase change in evaporator and condenser, and semi-empirical closure relations
• Physical transparency and replaceability of closure models are primary design goals
• Steady-state foundation first; dynamic seams declared and prepared
Scientific committee presentation · 2026
MPL2030 — MPL loop simulation library | 1 / 8
MPL2030 — MPL loop simulation library | 1 / 8
Notes: Welcome. This presentation describes the physical modelling framework we are developing for Mechanically Pumped Loop simulation within MPL2030.
Our central challenge is that MPL loops tightly couple global pressure, local enthalpy transport, two-phase thermodynamics, a pressurising accumulator, and empirical closure relations — all of which interact. A monolithic implementation makes any one of those elements hard to replace or validate in isolation.
The framework is designed to keep every physical assumption explicit and replaceable.

## Slide 2
The Physical Modelling Problem
A single-loop MPL with parallel evaporator branches
Accumulator (PCA/HCA)
Pump
Pipe (supply)
Evaporator A Q_in
Evaporator B Q_in
Condenser Q_out
Pipe (return)
Junction / Mixer
⬤
ṁ, ΔP_p
ṁ, h, P
Q_out → sink
(condenser)
P_ref
Variables
P pressure
h enthalpy
ṁ mass flow
x quality
Q_in heat load
Q_out heat rejection
ΔP_p pump rise
Loop pressure closure: the sum of pressure changes around any closed path must equal zero. Phase change occurs in the evaporator (two-phase) and condenser (condensation). Parallel branches share the same ΔP; branch flow rates are solver-determined.
MPL2030 — MPL loop simulation library | 2 / 8
Notes: This diagram shows the essential topology of a single-loop MPL with two parallel evaporator branches and one condenser.
The key physical coupling is the pressure loop closure: the pump provides a pressure rise that must exactly balance the sum of all distributed and localised pressure drops. The accumulator sets the absolute pressure reference.
In the two-phase regions — the evaporators and part of the condenser — enthalpy, quality, heat transfer and two-phase pressure drop are tightly coupled. Parallel branches add a branch maldistribution problem: the framework must determine how the total mass flow splits between branches.
The variables P, h, ṁ are the primary unknowns. Temperature, quality, density and phase are derived quantities.

## Slide 3
State Representation and Property Philosophy
Primary unknowns, derived quantities, and the (P, h) choice
SystemState (solver-owned)
Stored primary unknowns (flat ordered vector):
P pressure at each port-node
h specific enthalpy at each port-node
ṁ mass flow rate at each port-node
V_g accumulator gas volume (internal state)
ω pump shaft speed (named seam, frozen v1)
ṁ is NOT part of FluidState.
Ports carry NO values — connectivity only.
FluidState (P, h, identity)
Derived on demand — never stored:
T, T_sat, ρ, μ, k, σ, c_p, phase
Quality (vapour fraction):
x = (h − h_f(P)) / (h_g(P) − h_f(P))
Continuous across subcooled / two-phase /
superheated — no region-switching required.
PropertyBackend: CoolProp (default),
REFPROP, tabulated, or empirical — swappable.
Why (P, h)?
(P, h) is single-valued and continuous across all thermodynamic regions. Storing T or ρ beside (P, h) creates a second source of truth that can drift silently. In dynamics, h is the natural energy-equation variable; adding dynamics activates stored derivatives, it does not change the state representation.
MPL2030 — MPL loop simulation library | 3 / 8
Notes: The state representation is a foundational design decision.
SystemState is the solver-owned flat vector of all primary unknowns: pressure P, specific enthalpy h, and mass flow ṁ at every port-node, plus named internal states such as the accumulator gas volume V_g and the pump shaft speed ω.
FluidState is a pure value object (P, h, identity). It is ephemeral — constructed transiently when a property is needed and then discarded. All derived quantities — temperature, density, quality, viscosity — are computed on demand from the PropertyBackend. They are never stored.
The key equation is the quality relation: x = (h − h_f(P)) / (h_fg(P)). It is continuous and differentiable across the saturation dome, which is essential for Newton convergence without region-switching.
Mass flow rate ṁ is part of SystemState, not FluidState. FluidState is two numbers plus identity — nothing else.
Ports carry no values. They are connectivity declarations only.

## Slide 4
Architecture as Physical Responsibility Separation
A strictly acyclic layered dependency graph — dependencies flow in one direction only
Layer 0 — Inert data
Geometry | PropertyBackend
Layer 1 — Thermodynamic state
FluidState (P, h, identity) → PropertyBackend
Layer 2 — Interface
Port (connectivity only — carries no numerical values)
Layer 3 — Closure
Correlation (pure, stateless: evaluate(input) → value + validity)
Layer 4 — Modifier
Calibration (named multipliers on closure outputs — not on balances)
Layer 5 — Local physics
Component (geometry + correlations + calibration → residuals)
Layer 6 — Topology
Network (topology, loop closure, branch structure, pressure-reference wiring)
Layer 7 — Numerics
Solver (assembles residuals, drives convergence — contains NO physics)
Output
Result (converged state + invariant residuals + calibration report + tuple reference)
dependencies flow down only
Three sanctioned seams:
① Swap a Correlation → config change only
② Edit the Network topology → topology change only
③ Swap the Solver → numerics change only
The DAG guarantees none disturbs the others.
MPL2030 — MPL loop simulation library | 4 / 8
Notes: The architecture is a strictly acyclic layered dependency graph. Every concept has a layer, and dependencies are permitted only downward.
Layer 0 is inert data: Geometry and PropertyBackend. They know nothing above them.
Layer 1 is FluidState. It reads the PropertyBackend and nothing else.
Ports at Layer 2 are connectivity declarations only. They carry no numerical values.
Correlations at Layer 3 are pure, stateless closure relations. They receive a typed input struct and return a value plus a validity verdict. They do not know the component, the network, or the solver.
Calibration at Layer 4 applies named multipliers to closure outputs — never to the conservation equations themselves.
Components at Layer 5 own local physics. They contribute residuals and derivatives. They do not know their neighbours, the network, or the solver.
The Network at Layer 6 states what must hold: topology, loop closure, branch structure, pressure-reference wiring. The Solver at Layer 7 determines how to satisfy it numerically.
This layering is not software elegance for its own sake. It makes every physical assumption explicit, replaceable, and independently validatable.

## Slide 5
Governing Balances and Closure Seams
Conservation equations vs. closure relations — a strict distinction
Conservation equations (never scaled)
Mass balance at each junction:
Σ ṁ_in − Σ ṁ_out = 0
Energy balance (steady, per component):
Q̇ − Ẇ + Σ ṁ_in h_in − Σ ṁ_out h_out = 0
Pressure loop closure (per closed path):
Σ ΔP = 0
Pipe pressure gradient (per cell, 1D):
dP/dx = (dP/dx)_fric + (dP/dx)_grav + (dP/dx)_acc
= R* · (dP/dx)_fric,corr + ρg(dz/dx) + d(G²v)/dx
R* = calibration multiplier (friction term only)
Closure quantities (replaceable, validated)
Single-phase friction gradient:
(dP/dx)_fric from Churchill (1977),
Müller-Steinhagen-Heck, or user-supplied
Two-phase pressure drop:
Friedel, Müller-Steinhagen-Heck, …
(Phase 11 — in progress)
Heat transfer coefficient:
Shah, Gungor-Winterton, Kim-Mudawar, …
(Phase 11 — in progress)
Void fraction / two-phase density:
HEM-type admissible; framework is
closure-agnostic — slip, drift-flux,
regime-dependent closures are future options
Calibration firewall:
Calibration multipliers scale closure outputs only (friction gradient, HTC). They never scale conservation equations. A wrong calibration worsens the balance residual — it cannot produce a false-passing balance.
MPL2030 — MPL loop simulation library | 5 / 8
Notes: This slide makes the most important physical distinction in the framework explicit:
Conservation equations — mass, energy, and pressure loop closure — are inviolable physical laws. They are assembled by the solver from component contributions and network conditions. They are never scaled.
Closure relations — friction gradient, heat transfer coefficient, void fraction — are semi-empirical substitutes for unresolved microscale physics. They are swappable, validity-bounded, and the primary research seam.
The pressure gradient in a 1D passage is decomposed into three terms: friction, gravity, and acceleration. The calibration multiplier R* applies only to the friction term. Gravity and acceleration are first-principles physics — they are never fudged.
On void fraction and two-phase closures: HEM-type closures are admissible and may be used in early two-phase models, but the framework is closure-agnostic. Slip-flow, drift-flux, regime-dependent, and empirical void-fraction closures can be substituted through the same correlation slot without changing the conservation equations.
Single-phase friction is implemented via Churchill (1977). Two-phase DP and HTC correlations are in progress in Phase 11.

## Slide 6
Pump and Accumulator: Drive and Pressure Reference
Phase 10 — implemented at V1 fidelity
Pump — pressure-rise / map / command seam
Prescribed pressure rise:
ΔP_p = ΔP_setpoint · R_p
Performance-map evaluation:
ΔP_p = f(ṁ, ω) from interpolated map
Power / efficiency seam:
Ẇ_p ≈ ṁ · ΔP_p · v / η_p
v = specific volume (from FluidState)
Shaft-speed ω: named internal state (frozen v1)
Commands: speed setpoint or flow target
Pump does NOT know Network or Solver
Accumulator — pressure-reference component
PCA (pneumatic) pressure law:
P(V_g) = P_charge · (V_charge / V_g)^n
V_g : gas volume (internal state in SystemState)
Law slot — swappable:
PCA (implemented) | HCA (declared seam)
bellows / spring / gas-charged (future)
Ownership split:
Accumulator owns: law, value, geometry
Network owns: which node is the reference
Solver owns: global consistency
A second accumulator → topology validation error
Phase 10 status:
Pump map/command/power seam, accumulator PCA law, V_g internal state, and Network pressure-reference wiring are implemented and audited. Dynamic shaft-speed derivatives and full loop pressure convergence are Phase 11+ work.
MPL2030 — MPL loop simulation library | 6 / 8
Notes: Phase 10 is complete. These are the two components that drive and anchor the MPL loop.
The pump is modelled as a pressure-rise component. In V1 it supports a prescribed pressure-rise setpoint and interpolation from a performance map. The power/efficiency seam computes shaft power from mass flow, pressure rise, specific volume, and mechanical efficiency. Shaft speed ω is a named internal state; in V1 it is frozen (zero derivative). Dynamics will unfreeze it — no new state variable will be needed.
The accumulator is a pressure-reference component. For a pneumatic compensation accumulator (PCA), the pressure law is a polytropic relation between gas volume V_g and pressure. V_g is the stored internal state; pressure is derived from it.
The pressure-reference ownership is split deliberately: the accumulator owns the law and the value; the network owns which node is the reference and enforces that there is exactly one; the solver owns global consistency. This means a second accumulator is caught at topology validation, not as a numerical pathology.
HCA and other law types are declared as future seams. PCA is the implemented V1 closure.

## Slide 7
Next Development: HeatExchangerModel, Evaporator and Condenser
Phase 11 — in progress (foundation and ε-NTU checkpoints merged)
HeatExchangerModel
(component-internal strategy)
Strategies (not correlations):
ε-NTU (implemented — foundation+11B)
LMTD (planned)
Segmented marching (planned)
Moving boundary (declared seam)
→ PropertyBackend (fluid properties)
→ HTC correlations (Shah, KM, …)
→ ΔP correlations (Friedel, …)
→ Geometry (plate, microchannel, …)
→ Secondary BC (T_sink, ṁ_sink, cp_sink)
→ Discretization (Lumped / Segmented)
Q̇ (heat rate)
h_out (outlet enthalpy)
ΔP (pressure drop)
residuals
validity verdicts
calibration report
Key distinction:
A Correlation returns one local closure value. A HeatExchangerModel is a solution strategy that consumes correlations, geometry, secondary boundary conditions and the PropertyBackend to produce an integrated thermal result. ε-NTU is a HeatExchangerModel strategy — not a correlation.
Scientific opportunity — parallel evaporators and branch flow distribution:
Each branch carries its own HeatExchangerModel, geometry, HTC/DP closures, and flow condition. Branch flows are solver-determined from equal-ΔP conditions. This framework supports maldistribution studies natively through topology — no special-casing.
MPL2030 — MPL loop simulation library | 7 / 8
Notes: Phase 11 introduces the HeatExchangerModel, Evaporator, and Condenser.
The critical architectural distinction is that a HeatExchangerModel is not a Correlation. A Correlation returns a single local closure value — a friction factor, an HTC, a void fraction. A HeatExchangerModel is a complete solution strategy for a heat exchanger: it consumes HTC correlations, DP correlations, geometry, the PropertyBackend, and secondary boundary conditions, and it produces an integrated result — heat rate, outlet enthalpy, pressure drop, and residuals.
ε-NTU is implemented as a HeatExchangerModel strategy. It is not a correlation and does not belong in the correlation registry.
What is implemented so far: the HeatExchangerModel contract and registry, EvaporatorComponent and CondenserComponent wrappers, and the ε-NTU model with fixed-heat-rate and sink-inlet-temperature-and-flow modes including explicit PrimaryThermalMode and UAComputationMode.
LMTD, segmented marching, and moving-boundary models are planned but not yet implemented.
The parallel evaporator case is particularly important scientifically: the framework handles it through topology — adding a branch is a network edit, not a solver or component change. This makes maldistribution studies straightforward.

## Slide 8
Scientific Opportunities, Limitations and Validation Roadmap
"Architecture is used here to make physical assumptions explicit, replaceable and testable."
Scientific opportunities
• Parallel evaporators and branch maldistribution
• Correlation comparison studies (Shah vs Kim-Mudawar, etc.)
• HEM vs slip / drift-flux / void-fraction closure alternatives
• Accumulator influence on loop pressure stability
• DOE / parametric sweeps over geometry and operating point
• Dynamic modelling and transient response (future seams prepared)
• Control-oriented linearisation (MPC / ROM extraction)
Current limitations
• Steady-state only (dynamics: seams declared)
• 1D / lumped component contributions (segmented fidelity available)
• Correlations are semi-empirical and validity-bounded
• Two-phase HX physics (Phase 11) not yet complete
• HCA accumulator: declared seam, not yet implemented
• LMTD, segmented-march, moving- boundary HX: planned, not built
• Moving-boundary condenser: dynamic event detection deferred
Validation roadmap
Completed:
Phases 1–10 audited 2 301 tests passing
Unit: FluidState, Correlation, Calibration, Geometry, Pump, PCA
Network topology and assembly
Steady solver residuals
In progress:
HX model + ε-NTU (Phase 11)
Planned:
Kokate (2024) R-134a loop data
Li et al. (2021) Acetone data
Fujii (2004) validation data
MPL2030 experimental data (future phases)
"Architecture is used here to make physical assumptions explicit, replaceable and testable."
MPL2030 — MPL loop simulation library | 8 / 8
Notes: Let me close with an honest assessment of where we are and where we are going.
Scientific opportunities: The framework's explicit seams make it well-suited for correlation comparison studies — switching from Shah to Kim-Mudawar in an evaporator is a configuration change. Parallel evaporator branches with maldistribution are handled through topology. Accumulator stability, HEM versus slip-flow alternatives, and future dynamic and control-oriented work are all natural extensions.
Limitations — we are honest about these:
We are steady-state only today. Dynamic seams are prepared but not activated.
Two-phase heat exchanger physics — boiling HTC, condensation HTC, two-phase DP — are in progress in Phase 11 and are not yet validated against literature data.
HCA is a declared seam, not an implemented model.
LMTD and segmented-march strategies are planned but not built.
Validation roadmap: Phases 1 through 10 are audited and 2301 tests pass. Literature validation against Kokate (2024) R-134a data, Li et al. (2021), and Fujii (2004) is planned for Phase 12 and beyond. MPL2030 experimental data will enter as it becomes available.
The closing statement says it directly: the architecture is not a software goal in itself. It is the mechanism by which physical assumptions become explicit, testable, and replaceable.